## Slide 1: Interactive computation and visualization of wind farm flow fields based on model reduction
Yngve Heggelund
CMR Computing

## Slide 2: Norwegian Centre for Offshore Wind Energy - NORCOWE
Center for environment-friendly energy research (CEER)
50% RCN, the rest from industry and research partners
Combining Norwegian offshore technology and Danish wind energy competence
Research partners:
  Christian Michelsen Research AS (host)
  UiS
  UiA
  UiB
  Aalborg University
  Uni Research AS

## Slide 3: NORCOWE WP 4 – Wind farm optimization
Vision: Model system for optimizing the layout of (offshore) wind farms based on Computational Fluid Dynamics (CFD)
  Nowcasting: 2-120 seconds
  Power system integration
  Wind farm modelling

## Slide 4: Wakes
Wake effects caused by upstream turbines
  Reduces energy output of downstream turbines
  Increases material fatigue because of increased turbulence

## Slide 5: Objectives
Find a layout which minimizes the wake effects
Reduce the uncertainty of production estimates

## Slide 6: Motivation
Traditional approach: simplified wake models
  Often underestimates wake effects
CFD provides the state-of-the-art method for solving complex flow problems
CFD is computationally expensive – one simulation typically takes hours/days/weeks to complete
  Prohibits straightforward use in optimization of layout
We have to make some simplifications!

## Slide 7: Model reduction, background
Idea: Restrict the solution space to a reduced representative subspace
  Full dimension ~3 000 000 grid cells
  Subspace dimension ~100 unknowns
E.g. used for real-time visualization of fluid effects (Treuille et al. 2006)
Examples of other applications of model reduction for fluids
  Study of flow past a rectangular cavity (Rowley, 2002)
  Optimal rotary control of cylinder wake (Bergman et al., 2005)

## Slide 8: Model reduction, theoretical framework
Steady state RANS (Reynolds-Averaged Navier-Stokes) momentum equations
Seek solutions in a space spanned by an orthonormal basis (m n)
Any solution in the reduced space is a linear combination of the basis vectors
Constraint: Solutions should fulfil the force balance in the steady state RANS equations

## Slide 9: Model reduction, operator examples
Pressure operator
Projected to reduced space:
Advection operator is nonlinear
  Implies one operator matrix for each basis vector
  Can show that this can be expressed by a tensor of third order:
In this way the governing equations can be expressed in the reduced space
CFD discretization
Reduced order space representation

## Slide 10: Contructing a representative basis
Snapshots of CFD solutions for different placements of turbines
Singular value decomposition (SVD) to extract an orthonormal basis which minimizes the reconstruction error
A representative basis is critical for a good result!

## Slide 11: Tiles
Must be able to move turbines
Construct tiles which capture localized behaviour, which can be assembled at runtime
Couple tiles through matching the boundary conditions
Results in a system of equations represented by a large sparse block matrix
  Solving for the coefficients in each tile
  Trade-off between matching boundary conditions and fulfilling the steady state RANS equations

## Slide 12: Test case
Idealized system with three wind turbines and wind predominantly from the west
Where should turbine C be placed?
6 simulations with FLACS-Wind (CMR GexCon) for different positions of the back row turbine
A
B
C
The two most important modes in the basis

## Slide 13: Interactive tool for testing turbine positions
User can move turbines by dragging tiles
New flow fields and production estimates are calculated within seconds

## Slide 14: Demo